## Slide 1: Engineer’s guide to modern lab
Thomas Ferreira de Lima
tlima@princeton.edu

## Slide 2: Outline
8:20AM - Welcome and settling in. Macbooks charging. Internet connection ok etc.
8:30AM - Introduction, outline
8:45AM - An engineer's guide to modern lab control (part 1)
  What is version control / git (15 minutes)
  15-minute exercise
  Cloning and collaborating from github (15 minutes)
  A small intro to UNIX and bash
  Digital security + private key authentication + 2FA
  Break demo: have all connect to cassander/github with their key
10:00AM - break (installation of homebrew + virtualenv + python3 + jupyter)
10:15AM - Messing around with python
  Features of a programming language (coming from MATLAB) - python as example
  Scientific computing: numpy, scipy and matplotlib
  Getting comfortable reading source code and documentation
    The init file
    doc docstrings
    navigating modules with sublime or github.
  Awesome python data processing and plotting demo
11:15PM - Q&A session about individual projects (part one)
12:00PM - Lunch break
1:30PM - An engineer's guide to modern lab control (part 2)
  Why centralized control
  GPIB, USB and Serial protocols
  Ethernet, TCP, IP, Socket
  Instruments, hosts, servers, clients
  Building a server machine in your lab: basic concepts
  Saving and backing data up (version control?)
2:15PM - Break
2:30PM - Demo sessions (Eric, HT, Tait et al.)
  HT: SIMPEL: quick overview of cython integration
  Eric: Live experiment control
  Lamia: Parsing data and regularization algorithm
  Tait: Virtual experiment
3:30PM - Walkthrough of lightlab package
4:15PM - Princeton Resources
4:30PM - Q&A session about individual projects (part two)
5:30PM - fin

## Slide 3
Git!

## Slide 4: UNIX (Unix-like) systems
Unix is a family of operating systems derived form the original AT&T Unix. It follows a particular software philosophy:
  “Although that philosophy can't be written down in a single sentence, at its heart is the idea that the power of a system comes more from the relationships among programs than from the programs themselves. Many UNIX programs do quite trivial things in isolation, but, combined with other programs, become general and useful tools.” Brian Kernighan and Rob Pike,1984
Linux is a unix-like system, but was developed for the GNU Project, which was created because Bell Labs began selling Unix as proprietary after AT&T divested.
  Three important linux distributions are: RedHat (server friendly, $$$$), CentOS (free version of RedHat), and Ubuntu (user-friendly)

## Slide 5: Unix-like permissions
How does the system know a user exists?
  It simply looks into /etc/passwd and checks the user id, group id, name, home folder and shell program. (does not work in mac)
  Similarly for groups, it checks /etc/groups
There are two kinds of users: superuser, system users and regular users.
  Every program must be run by one user at one time.
  Each program will have access to, and only to, all files accessible by its user.
  Security feature: superuser can override any permission
  `ls -l` shows the output below

## Slide 6: Common mistakes involving permissions
Files created via sudo cannot belong to a user
Accidentally changing modes recursively
Accidentally changing ownership
Miscellaneous features of Unix-like system
Symbolic links
Mount points
Manual pages
Terminal editors (vim, nano)

## Slide 7: Unix-like shell
A shell is an interactive program that is created at login and survives during the entire session.
The most common shell is called bash (bourne again shell, named after GNU’s reboot of Stephen Bourne from Bell Labs). All examples in this tutorial are going to use bash.
At startup, the file ~/.bash_profile is read, which typically references ~/.bashrc, which then references /etc/bashrc, which executes all files in /etc/profile.d/
Variables created in a shell persist as environment variables, so be careful
Use `bash` to execute scripts in a new subshell, and use `source` to execute scripts in the same shell
Read about stdin, stdout and stderr

## Slide 8: Unix-like program suite
Bash finds the program associated with a particular command by searching the folders in the environment variable PATH
Other programs will need environment variables to function properly. Notorious example is python, which sometimes need a PYTHON_PATH
Check all environment variables with `env`
Check PATH variable with `echo $PATH`
You can transform your own script to an executable program by:
  attaching #/bin/bash in the first line, indicating the program that runs the script
  giving executable permissions to the file
  copying or linking the file to a folder in $PATH
Another possibility to create a command is to add a function in your bashrc or bash_profile
If you are wondering where to find a certain command, try checking your bashrc and your $PATH. The command `which` is very useful.

## Slide 9: Digital security and Private key authentication
Diffie-Hellman key exchange
Passwords are nothing but authenticators. It is the way the machine know you are you.
For a server, it is very important because it’s the only way the user can verify it’s identity. (TLS certificates, or SSH key fingerprint)
For a user, a public key is a method of 2FA, but only if you lock the key with a passphrase!
Otherwise it is a little more secure because you are safe even if the server is hacked.
The only disadvantage: a little more work.

## Slide 10: Common 2FA: Time-based One-Time Password
The Time-based One-Time Password algorithm (TOTP) is an algorithm that computes a one-time password from a shared secret key and the current time.
According to RFC 6238, the reference implementation is as follows:
  Generate a key, K, which is an arbitrary byte string, and share it securely with the client. (e.g. via a QR code)
  Agree upon a T0, the Unix time to start counting time steps from, and an interval, TI, which will be used to calculate the value of the counter C (defaults are the Unix epoch as T0 and 30 seconds as TI)
  Agree upon a cryptographic hash method (default is SHA-1)
  Agree upon a token length, N (default is 6)
Token generation:
  TC = floor((unixtime(now) − unixtime(T0)) / TI),
  TOTP = HOTP(SecretKey, TC),
  TOTP-Value = TOTP mod 10d, where d is the desired number of digits of the one-time password.

## Slide 11: Python as programming language

## Slide 12: GPIB, USB, Serial
GPIB hardware interface options
USB (straightforward)
Serial to USB < $30
GPIB-USB about $600
PCI-GPIB about $740
GPIB-ENET/1000 about $1400

## Slide 13: VISA (Virtual Instrument Software Architecture)
VISA is a standard for configuring, programming, and troubleshooting instrumentation systems comprising GPIB, VXI, PXI, Serial, Ethernet, and/or USB interfaces.
The VISA specification has explicit bindings to Visual Basic, C, and G (LabVIEW’s graphical language). However, you can use VISA with any language capable of calling functions in a shared library (.dll, .so, .dylib). PyVISA is Python wrapper for such shared library ... and more.

## Slide 14: Ethernet LAN
A little bit about networks and internet
An 8-port switch

## Slide 15: Understanding Protocols: TCP/IP
OSI 7-layer model (concept)
TCP/IP can be understood under the OSI framework
It goes from high level (application) to low level (bits and voltages)

## Slide 16: Understanding Protocols: TCP/IP
A packet contains a lot of headers that are used for routing, switching, communication control etc.

## Slide 17: VISA Socket application
Two of our instruments are controlled directly through the LAN using sockets.
VISA is the application, socket controls the session (open, close, alive, dead etc.), TCP/IP are the transport and network protocols, and Ethernet is the physical one.
We can also use pyvisa to talk to a Labview socket server.
https://forums.ni.com/t5/Example-Program-Drafts/Python-LabVIEW-TCP-IP-socket-communication/ta-p/3537049
Ask Alex Tait if you are interested in learning. Or copy paste his code from Andromeda.
More info: https://www.edn.com/electronics-news/4378802/Linux-controls-instruments-through-Ethernet
https://www.rohde-schwarz.com/us/driver-pages/remote-control/3-visa-and-tools_231388.html

## Slide 18: Socket application
If you want to communicate to an Arduino, you have three options:
  Serial (USB)
  Ethernet (RJ45 cable)
  WiFi (wireless)
Example from: https://arduino.stackexchange.com/questions/35682/how-to-run-tcp-socket-server-on-arduino-uno-wifi
Should be straightforward. Use core python packages serial or socket.
Arduino ethernet
Arduino WiFi shield

## Slide 19: Princeton Resources
HPCRC offers computer clusters for heavy load computations. Also some more obscure services, like technical support and workshops.
They also offer free private github repositories if you fill a form: https://www.princeton.edu/researchcomputing/faq/how-do-github-permissions/
Attend all mini-courses they offer. They are entry-level. https://www.princeton.edu/researchcomputing/education/mini-courses/
Student developer pack: a lot of free tools for students, including github and cloud services: https://education.github.com/pack